Red Dragon

Matsuura RA1F

Start-up Instructions

- Open the air valve on the right side of the machine.  The handle will be parallel to the floor when its on.  You should hear the booster chugging, if not check other upstream valves.

- Turn on the breaker – left rear of the machine.

- Press the square green Power on button on the control console, wait for the computer to boot.

- Press the power button again, this should power up the motor drives.  If you get an alarm, wait a few minutes then press it again.  It will not report errors when all the drives in the right control box all show 2 green LEDs.

- Set the mode to Origin  - a circle with an + in it.

- In the lower right corner of the control console, set the axis selector to X

- Press the '-' button for a second, the stage should move.  Then press the '+' button, release it and wait for the X axis to get to the home position.  The X home LED should light.

- Repeat step 7 with the axis button set to Y then Z.  This should zero all the axis.

- You are ready to mill

Note:  To start the spindle set the mode to MDI, enter 'M3 S3000' press WR.  This will enter the command to run the spindle clockwise at 3000 RPM.  Press the green start button on the bottom of the control panel to execute the command and start the spindle.  M4 will run the spindle counter clockwise, and M5 without anything else will stop the spindle.

Updated 1/19/15 TJG