Tormach Vertical Machining Center

1.	Startup

- Main power

- Air

- Check Coolant level

- Pull oiler handle

- Wait for software

- Release E-Stop

- Press Start

- Click on Reset

- Reference Z

- Reference X & Y

2.	Workpiece mounting

- Remove burrs

- Never clamp on sawed edges

- Use parallels to raise workpiece in vise so tooling doesn’t cut into the vise.

- Tighten vise until snug.

- Hammer on workpiece to seat on parallels.

- Tighten vise completely

- Parallels should not move if piece is down all the way.

3.	Tool mounting

- Clean inner taper surface and threads of collet holders

- Use collet size to match tooling

- Attach collet to nut before placing in holder

- Tighten but do not over-tighten

4.	Tool offsets

- Make sure granite is clean

- Zero height gauge before each tool height measurement

- Wipe off TTS shaft and ring before placing into granite

- Make sure height measurement is stored for correct tool number

5.	Work offsets

- Use same origin point as drawing.  Usually this is the lower left corner or the center of the piece.

- Spin edge finder at 1000 RPM.

- Enter -.1 as the work offset for the axis to account for edge finder radius.

- Double check origin location by jogging to X0 Y0 with Z raised to clear the part.

- Use a measured tool and a piece of paper to determine Z zero offset.

6.	Conversational programming

- DOC (Depth Of Cut) for the spot drill is actually the Z dimension it should drill to.

- Rather than store all operations in a single file the first time a part is made store each operation is a separate file.  That way you can make changes to the operation easily.  The files can be combined after they are proven.

7.	Running a program

- Prove tool paths by subtracting an inch from the workspace Z and running the code.  After you are sure where the tool will move to then add the inch and run again.

- Adjust the coolant hose to spray down onto tool tip.

- Keep an eye on the coolant level and chips in the coolant strainer.

7.	Cleanup

- Remove all tooling from ATC

- Remove all tooling and collets from collet holders, wipe down, and place into racks.

- Use the vacuum to remove all of the chips from the machine.

- After vacuuming use the air hose to blow missed chips out of corners and vacuum again.

- Clean out pan on top of coolant tank.

- Vacuum the carpet leading into the meeting room and the floor area around the machine.

8.	Shutdown

- Press E-Stop

- Click on Exit button on screen

- Turn off main power when notified by software.

- Turn off air

- Lock the tool cart

- Lock the tool cart key into the key vault.